## Slide 1
Compare EKF&NAVSAT vs Lio-sam
EKF & NAVSAT_TRANSFORM
Lio-sam
발표자 : 이담

## Slide 2
Drone_localization typical setup (rqt_topic)
  /velodyne_lidar/fix (sensor_msgs/NavSatFix)
  /velodyne_lidar/imu (sensor_msgs/imu)
  /odometry/navsat (nav_msgs/Odometry)
  /odometry/filtered (nav_smgs/Odometry)
  /lio_sam/mapping/odometry (nav_msgs/Odometry)

## Slide 3
NAVSAT launch file
EKF launch file

## Slide 4
rqt graph

## Slide 5
rqt graph_EKF&NAV

## Slide 6
Basic setting : EKF_template.yaml
Odometry 관련 parameter
  Odometry/navsat은 아래와 같음

## Slide 7
GPS Topic name : rostopic echo /velodyne_lidar/fix
IMU Topic name : rostopic echo /velodyne_lidar/imu

## Slide 9
Navsat_transform_template.yaml
  Yaw_offset defalt = 0
  LIO-SAM transforms IMU raw data from the IMU frame to the Lidar frame : (x - forward, y - left, z - upward)
  → 즉, Lio-sam의 pose값은 y축의 기호가 반대로 나옴

## Slide 10
Navsat_transform_template.yaml
  yaw-offset defalt unit is RADIAN
  yaw를 90도 돌려, lio sam과 ekf의 pose값을 비교할 수 있음

## Slide 11
Lio-sam
  Config file topic 수정, config/params.yaml
  In simulation, LIDAR and imu value

## Slide 12
Lio-sam & gazebo simulation 실행

## Slide 13
1. EKF Parameter 수정
  Frequency defalt 30 > 10
  불안정한 값을 자주 받아서 그런듯 함
Pic. default graph
Pic. Modify frequency graph

## Slide 14
2. EKF Parameter 수정
  odom, imu config 및 odom pose, twist 추가
  odometry > pose(pose, orientation) / twist(linear, angular)
  imu > orientation, angular velocity, linear accelation
Pic. first graph
Pic. later graph

## Slide 15
3. EKF Parameter 수정
  World frame defalt odom > map
  GPS는 이산적이고 절대적인 값이므로 world frame : map
Pic. world frame map graph

## Slide 16
4. EKF Parameter 수정
  Process_noise_covariance 수정 > Lio-sam covariance
Pic. first graph
Pic. later graph

## Slide 17
4. EKF Parameter 수정 – 최종
  Frequency(30), world frame(map), odom/imu config, odom pose/twist, process noise covariance
  Yellow arrow : lio sam / Blue arros : filtered odometry / Purple circle : ekf covariance
Pic. compare graph_final

## Slide 18
Position set (0, 0, 10)
  odometry/filtered와 lio_sam/mapping/odometry 비교
Pic. Compare position

## Slide 19
Position set (5, 5, 5)
  odometry/filtered와 lio_sam/mapping/odometry 비교
Pic. Compare position